## Slide 1: REKF and RUKF for Pico Satellite Attitude Estimation in the Presence of Measurement Faults A Robust Approach to Sensor Malfunctions
Based on Paper by: Halil Ersin Söken and Chingiz Hajiyev

## Slide 2: Problem Statement
Pico satellites rely on magnetometers and Kalman Filters (EKF/UKF) for attitude estimation.
Standard filters assume fixed noise characteristics. They lack the capability to adapt to sensor malfunctions (e.g., abnormal measurements or sudden shifts).
When a sensor fails, standard filters produce inaccurate results and diverge over time.
Pico satellites have limited computational power; complex robust methods (like parallel filters) are often too heavy. A lightweight, robust solution is required.

## Slide 3: Problem Setup
State Variables: 6-dimensional vector containing Euler angles (Roll φ, Pitch θ, Yaw ψ) and body angular rates (ωx ,ωy ,ωz ).
Measurements: Earth magnetic field vector components measured by a Three-Axis Magnetometer (TAM).
Noise Assumptions: Process and measurement noise are zero-mean Gaussian white noise, Uncorrelated process and measurement noise.
Gap Addressed: Developing a fault-tolerant estimation algorithm that modifies the filter gain only when measurements are corrupted, without high computational cost.

## Slide 4: Method Overview
Key Concept: Measurement Noise Scale Factor (MNSF) or S(k).
Mechanism:
  The filter monitors the "innovation" sequence (residual error).
  If the actual error exceeds the theoretical covariance, a fault is declared.
  The algorithm calculates S(k) to inflate the measurement noise covariance R(k).
Result: The Kalman Gain K decreases, reducing the weight of the faulty measurement in the state update.

## Slide 5: Model

## Slide 6: Simulation Setup
Simulation of Pico Satellite Dynamics on MATLAB
Circular Orbit, Altitude r = 550 km, Inclination I = 97°.
Initial Conditions and Noise:
  Magnetometer standard deviation: σm= 200 nT
  Gyro random error: σv= 9.19 X 10-7 rad/s.
Experiment:
  Duration: 500 seconds.
  Fault Injection: A constant bias term is added to one magnetometer measurement at t = 300s to simulate a malfunction.

## Slide 7: Results
Standard EKF: At t = 300s (fault injection), the Roll angle estimation error spikes significantly and does not recover.
REKF: Detects the fault. The error increases slightly but remains bounded and accurate compared to EKF.
MNSF Behavior: The Scale Factor S(k) stays at 1.0 during normal operation and spikes to
6 X 108 at t = 300s to reject the fault.

## Slide 8: Comparisons
Like the EKF, the standard UKF produces unreliable results when measurements are faulty.
RUKF maintains estimation characteristics throughout the malfunction.

## Slide 9: Interpretation & Insights
Why it works: The huge increase in S(k) effectively tells the filter to "ignore" the current measurement update and rely on the system model propagation. This isolates the fault.
Why RUKF > REKF: The UKF captures higher-order statistics of the system nonlinearity using sigma points, whereas REKF relies on linearization (Jacobians), which introduces errors in highly nonlinear dynamics.
Practicality: The algorithm adds minimal computational load (simple trace calculations), satisfying the 10% mass/power constraint of pico satellites.

## Slide 10: Conclusion
This paper introduced REKF and RUKF with an adaptive Measurement Noise Scale Factor (MNSF) to handle sensor faults
Both robust filters outperform their optimal counterparts during malfunctions.
RUKF is the preferred method for pico satellites as it offers higher accuracy than REKF without significant computational burden.
Simple adaptive scaling of noise covariance is an effective, lightweight strategy for spacecraft fault tolerance.